## Slide 1: Mechanical Engineering Master’s Thesis Defense
Candidate: Jakob Frabosilio
Committee: Dr. John Ridgely (chair)
Charlie Refvem
Dr. Siyuan Xing

## Slide 2: Presentation Outline
Introduction
Ground-Truth Positioning System
Acoustic Positioning System
Absolute Orientation and Dead Reckoning
Kalman Filtering
Data Collection and Results
Conclusion and Future Work

## Slide 3: Self Introduction
Jakob Frabosilio
Started B.S.M.E. in 2018
Started M.S.M.E. in 2022
Member of Cal Poly Mustang Band for all six years of college
First mechatronics project in Sep 2019
Dark Ride: CAPED Project
Designed ride vehicle

## Slide 4: Problem Definition
Autonomous Underwater Vehicles (AUVs) are used to collect data in the ocean and require position information
Examples: shipwrecks, ocean floor mapping, phytoplankton level monitoring, search-and-rescue, and so much more
Problem: GPS does not work underwater!
Need a way to reliably determine AUV location when submerged for long periods of time

## Slide 5: Existing Solutions
Solution | Benefits | Drawbacks
GPS/GNSS | Moderate accuracy (< 3m) Does not drift over time | Does not work underwater (surfacing required)
Dead Reckoning | High accuracy for small ΔT Local solution | Estimate drifts over time High sampling rate required
Simultaneous Localization and Mapping (SLAM) | Creates map of environment Local solution | High computational cost Requires precise SONAR
Acoustic Positioning | Sound travels far in water Does not drift over time | Requires line-of-sight Noise pollution concerns
Muometric Positioning | Works anywhere on Earth Very high accuracy (3.9cm) | Very recent research (2023) Not many implementations

## Slide 6: My Approach
Combine acoustic positioning, dead reckoning, and GPS
Buoy on surface of water with GPS and acoustic transmitter
GPS provides absolute reference to global frame
AUV with microphone array and dead reckoning equipment
Acoustic positioning provides relative reference to GPS
Dead reckoning provides short-term relative position
Use sensor fusion to blend three methods
Test system above-water, extrapolate to underwater
Lower cost, no waterproofing req’d, lower speed of sound

## Slide 7: Functional Diagram

## Slide 8: High-Level Overview
Use ground-truth positioning system to verify accuracy, simulate motion of AUV underwater
Transmitter sends out a pulse of ultrasonic sound
Four microphones on receiver array record the pulse
Time difference between microphone signals is calculated
Position of transmitter estimated using time differences
Array orientation and dead reckoning estimated using IMU
Fuse estimates with a Kalman filter
Position estimate of array is compared to ground-truth

## Slide 9: Ground-Truth Positioning System

## Slide 10: Design Inspiration
Need a 6-degree-of-freedom (6-DOF) actuator
Low cost, high research potential, high accuracy
Stewart platform (“hexapod”) is 6DOF
NASA research, stack hexapods to increase range
Use in spacecraft equipment manipulation

## Slide 11: Previous Works
CSC 580: Artificial Intelligence, designed deep RL agent to control a stacked hexapod platform
Nicolas Jeanmonod, engineer, designed open-source hexapod controller for ESP32 microcontrollers
Thesis builds off Nicolas’ work, modifies it to work with four stacked platforms

## Slide 12: Design Overview
Four identical stacked hexapod platforms
Reduces complexity and cost
Independent control for each platform
Current version: identical control
3D-printed and off-the-shelf components
Purchased from Amazon and Ace Hardware
Total cost: $292
Name: Four-Stacked Hexapod Isometric Platform
Fo-SHIP (pronounced “faux ship”)

## Slide 13: Mechanical Design
Designed five unique 3D-printed plates
Re-use simplifies manufacturing process
Heat-set inserts allow threaded connections
Electrical components have mounting slots
Base plate mounts to wooden base for stability
End effector plate has mounting holes for attaching array

## Slide 14: Electrical Design
Multiple components need to interact and communicate
Microcontroller (ESP32) controls motors, makes decisions
Servo motors connected to PCA9685 motor driver
IMUs (angle sensors) detect orientation of each platform
DC power supply gives steady, high-amp electrical power
Different communications protocols between devices
ESP32 talks to motor drivers, IMUs over I2C
ESP32 talks to laptop, STM32 over serial (UART)

## Slide 15: Wiring Diagram

## Slide 16: Manufacturing and Assembly
Plates 3D-printed in Mustang ‘60 Machine Shop
Wooden base fabricated in Mustang ‘60
Fo-SHIP assembled in stages
Electrical boards attached to base plates, heat-set inserts installed with soldering iron
Servo motors sandwiched between plates
Servo arms, threaded rods attached to servo output, then connected to next platform with ball joints
Platforms assembled from base to top, wires secured with cable ties after assembly

## Slide 17: Software Overview
Written in C++ for ESP32 microcontrollers (MCUs)
Main tasks and functions:
Calculate servo angles for a desired position
Move each platform to that position
Determine XYZ position of end effector
Communicate w/ acoustic positioning system MCU (STM32)
Send data to laptop for future processing / storage
Demonstration functions:
Full range-of-motion, active tracking of transmitter

## Slide 18: Single-Platform Inverse Kinematics
Given a desired top plate position, what should servos set to?
Solution w/ linear actuators is simple
Move top plate to desired position
Determine coordinates of P
Set each actuator length to BP
With rotary actuators, more complex
Define triangle ΔBAP
BA must be length of servo arm
AP must be length of threaded rod
Use trig identities, quadratic formula
__
B
A
P
__
__

## Slide 19: Multi-Platform Forward Kinematics
Orientation of each platform affects the one above it
Position of each platform given in local frame
Can be converted to global (“test”) frame
Describe each platform with two vectors
Translation – how does top plate shift in XYZ?
Rotation – what is normal vector to top plate?
Assume base of Fo-SHIP is on XY plane
Rotate each translation vector by orientation of platform beneath it, stack end-to-end

## Slide 20: Servo Offset Calibration
Each servo motor has slightly different “zero” angle
Servo horns must be level for accurate positioning!
Manufactured go/no-go gauge in machine shop
Servo angle offsets adjusted in software until level
Max. angular misalignment of 3.7° between adjacent servos

## Slide 21: System Validation
Need to validate position estimate of Fo-SHIP end effector
Tested min/max of each axis, measured true position
Many potential sources of error:
Servo angular misalignments, incorrect platform dimensions
“Slop” in system compounds with each platform
Lower accuracy for larger angles/moves
Avg. error: 7.4mm Max. error: 21.1mm

## Slide 22: Fo-SHIP Motion Demonstration

## Slide 23: Acoustic Positioning System

## Slide 24: Long, Short, and Ultrashort Baselines
Main distinction in acoustic positioning systems is baseline
Baseline: spacing between receiver elements
Long baseline (LBL) uses spacing of >100m, fixed receivers
Ultrashort baseline (USBL) is <10cm, less than one wavelength
Short baseline (SBL) is in-between, mics usually on ship hull

## Slide 25: Inverted Short Baseline
USBL and SBL systems have receivers at surface of water
Inverted USBL (iUSBL) systems put receiver module on AUV
Single receiver module / housing
Inverted SBL (iSBL) would put receivers on body of AUV
Spacing can be > one wavelength
Receivers can be anywhere on body, not constrained to single module
Greater spacing = better accuracy
Similar implementations exist, but none called iSBL (except this one!)

## Slide 26: Receiver Array Mechanical Design
Array mimics body of AUV
Receivers spaced 25cm apart
Array made from laser-cut acrylic for lightweighting and lowering cost
3D-printed 90° adapter for attaching to Fo-SHIP end effector
Microcontroller, IMU, and breadboard mount on face of array
Coordinate system is NED

## Slide 27: Receiver Array Electrical Design
STM32H723 high-performance microcontroller
Records at >1 million samples per second
Has >200kB of RAM for temporary data storage
High CPU clock speed of 550MHz
Communicates with Fo-SHIP ESP32 over UART
Reads from IMU over I2C
Connected to laptop with USB for debugging
Records from four microphones at 851.4kHz each
Smoothing capacitors for filtering electrical noise

## Slide 28: Receiver Array Wiring Diagram

## Slide 29: Active Band-Pass Filter Design
Raw ultrasonic receivers not sensitive enough, need boosting
Active band-pass filter provides amplification and filtering of non-40kHz signals (receiver operating frequency)
Adds 1.65V DC offset to use full range of ADCs
Provides gain of 34.5dB at operating frequency

## Slide 30: Active Band-Pass Filter PCB
Custom printed circuit board (PCB) designed in Eagle
Manufactured by OSH Park
Components ordered from Mouser Electronics
Uses common resistor and capacitor values to lower cost

## Slide 31: Receiver Array Assembly
Active band-pass filter PCBs soldered by hand
Soldered breadboard used to route power and mic signals
Wires cut to connect PCBs to breadboard and STM32
Array frame assembled with screws, attached to 90° adapter
STM32, IMU, and breadboard secured to face of array with screws and adhesive
Wires secured with cable ties

## Slide 32: Transmitter Hardware Design
STM32F411, small form factor microcontroller
Only need two GPIO pins, one timer
Problem: how to drive 40kHz ultrasonic transmitter?
Multiple motor drivers tested, all failed
High update rate required (>80kHz), high voltage (12V)
Charlie donated optical-switching motor driver, successfully drives transmitter (thanks Charlie!)
Tested multi-element transmitter, cause phasing issues; single transmitter used for testing

## Slide 33: Engineered Ultrasonic Waves
Operating at receiver resonant frequency for best range
Problem: resonance increases sensitivity, but adds ringing!
Sending just one pulse (12.5us) rings for 2300us
Sharper pulse recordings = better time-differencing
UK researchers designed waveform to reduce ringing by 81%
Wave pattern: 5 in-phase 6 out-of-phase 3 in-phase

## Slide 34: Transmitter Software Design
Implemented engineered waves into transmitter code
One “pulse” = one wave pattern (5-6-3)
Approximated pattern as square wave
Original goal was to transmit GPS coordinates over ultrasonic
Convert coords to character string: “x=20” -> “x”, “=“, “2”, “0”
Convert to ASCII 8-bit representation: “x” -> “01111000”
Send one pulse for 1s, wait (no pulse) for 0s
Currently sending random8-bit character using above system
Added 6-bit header to “trigger” recording on STM32
Sending pulses at 2000kHz, one per 0.5ms

## Slide 35: Transmitter Output

## Slide 36: Finite-State Machine Representation
Acoustic positioning system program (running on STM32) has five main states
Initialization: starting timers, setting up algorithms, etc.
Triggering: checks for acoustic pulse every 0.1ms
Full Recording: once detected, records for 2.4ms
Recording Validation: checks if recording actually contains the acoustic pulse (a “good recording”)
Data Processing: converts a good recording to a new position estimate and sends data to Fo-SHIP ESP32

## Slide 37: Finite-State Machine Diagram

## Slide 38: Analog-to-Digital Converter Setup
Analog-to-digital converters (ADCs) can measure voltages between 0 and 3.3V on STM32 GPIO pins
12-bit resolution (0.81mV) used, 0.42us per conversion
If sequential (Mic0 -> Mic1 -> …), max sampling rate is 595kHz
Using MultiMode (dual ADC), can double max sampling rate
Primary ADC triggers secondary, two conversions at once

## Slide 39: Triggering State
After initialization, first step is to check for an incoming pulse
Active band-pass filter removes non-40kHz audio
Assume any large readings from the ADC -> pulse incoming
Record 64 samples from each mic, check if any five samples in a row exceed a threshold; if so, pulse detected
One 40kHz wave -> 21.3 samples, five samples is enough
More samples/mic -> longer trig time -> less recording time
64 is good middle-ground, takes 0.1ms to record and check
If any mic exceeds threshold, move to full recording state
Otherwise, repeat triggering process

## Slide 40: Full Recording and Validation States
Full recording, 2048 samples per mic (2.4ms / 7ms full pulse)
IMU processing halted during full recording to prevent noise
Once saved, need to verify that recording contains pulse
Calculate standard deviation for each microphone signal
If std. dev. of all four mics > threshold, then recording is there
Threshold set just above ambient noise level
Area for improvement: use average of std. dev’s to determine how much to trust an acoustic measurement?

## Slide 41: Determining Time Shifts
Problem: need to find time shift between four mic signals
Assume signals are identical in shape, but time-shifted
Compare only two signals at a time
Solution: use cross-correlation!
Shifts signals over each other, peak of output shows time shift

## Slide 42: FFT Cross-Correlation Theory
Problem: cross-correlation is very slow
Solution: use fast Fourier transforms to speed up computation
Cross-correlation ≈ convolution
Convolution in time domain -> multiplication in frequency domain
Convert signals to freq. domain using FFT, multiply signals, then convert back to time domain with inverse FFT
Output is equivalent to normal method, but takes 99.9% less time (nsamples=4096)

## Slide 43: FFT Cross-Correlation Code
FFT cross-correlation implemented in C using arm_math.h
Three comparisons: mic0 vs mic1, mic0 vs mic2, mic0 vs mic3
Only three unique pairs; choice of mic0 is arbitrary
For each pair:
“Flip” second signal
Take FFT of both signals
Multiply results of FFTs
Take inverse FFT of product
Find maximum of output
Convert index from sample# to time

## Slide 44: Rotating the Receiver Array
Before converting time shifts to position, need to account for orientation of receiver array relative to test frame
Current orientation is known (Madgwick filter in background)
Create 3D coordinates for each microphone based on config
Rotate each point by current orientation of array
Now, position of each microphone is known in test (global) frame!

## Slide 45: Residual Function
Position of each mic, and time shift between mics, is known
How to find transmitter position based on this?
Define a residual function r(tx_guess, mic_coords, time_shifts)
tx_guess: guess for transmitter coords in 3D (in test frame)
Calculate distance from tx_guess to each microphone
Convert to time-of-arrival (TOA) using speed of sound in air
Subtract TOAs between mics to get estimated time shifts
Find difference between estimated and measured time shifts
If tx_guess is at true transmitter position -> residual is zero!
If tx_guess is very far from true position -> larger residual

## Slide 46: Hooke-Jeeves Search Algorithm
Most likely transmitter position is minimum of residual function
Problem: need a way to find the minimum of 3D function
Solution: Hooke-Jeeves search algorithm!
Start with some initial position estimate
Test points s distance away in each dir.
Move in direction of lowest residual, with step size s, until residual begins to grow
Cut step size in half and test new dir’s
Halt when exit condition is met
Always converges, is very accurate for this residual function

## Slide 47: Incorporating Transmitter Position
Hooke-Jeeves search returns position of transmitter relative to center of receiver array
Position of transmitter already known (GPS buoy)
Want to know position estimate of receiver array!
Receiver position = transmitter position – relative position
Finally, single estimate for center of receiver array using only acoustic measurements!
Position estimate in test frame
Can compare to true position (Fo-SHIP)

## Slide 48: Single-Pass Overview
Transmitter sends an acoustic pulse towards receiver array
ADCs trigger, pulse is recorded on four mics and verified
Time shift between signals found using FFT cross-correlation
Position of each microphone rotated using current orientation
Hooke-Jeeves search finds minimum of residual function
Returns position of transmitter relative to center of array
Use known transmitter location to get position estimate of center of receiver array in test frame

## Slide 49: Absolute Orientation and Dead Reckoning

## Slide 50: Measuring Orientation
Transmitter

## Slide 51: MEMS IMUs
Transmitter

## Slide 52: IMU Calibration
Transmitter

## Slide 53: Sensor Fusion Algorithms
Transmitter

## Slide 54: Madgwick Filter Overview
Transmitter

## Slide 55: Madgwick Filter Theory
Transmitter

## Slide 56: Madgwick Filter Implementation
Transmitter

## Slide 57: Madgwick Filter Tuning
Transmitter

## Slide 58: Dead Reckoning Overview
Transmitter

## Slide 59: Velocity Drift Compensation
Transmitter

## Slide 60: Dead Reckoning Implementation
Transmitter

## Slide 61: Dead Reckoning Validation
Transmitter

## Slide 62: Live Data Collection Demonstration

## Slide 63: Kalman Filtering

## Slide 64: Kalman Filter Introduction
Transmitter

## Slide 65: Airplane Example
Transmitter

## Slide 66: Kalman Filter Overview
Transmitter

## Slide 67: Initialization Step Theory
Transmitter

## Slide 68: Prediction Step Theory
Transmitter

## Slide 69: Update Step Theory
Transmitter

## Slide 70: Software Implementation
Transmitter

## Slide 71: iSBL Kalman Filter Design
Transmitter

## Slide 72: iSBL-SF Kalman Filter Design
Transmitter

## Slide 73: Kalman Filter Tuning
Transmitter

## Slide 74: Data Collection and Results

## Slide 75: Testing Plan
Transmitter

## Slide 76: Test Environment
Transmitter

## Slide 77: Data Collection Summary
Transmitter

## Slide 78: Stationary vs Moving Accuracy
Transmitter

## Slide 79: Gradual vs Rapid Movement Accuracy
Transmitter

## Slide 80: Effect of Distance on Accuracy
Transmitter

## Slide 81: Effect of Angle on Accuracy
Transmitter

## Slide 82: Evaluating Normality
Transmitter

## Slide 83: Overall Accuracy
Transmitter

## Slide 84: Active Tracking Demonstration

## Slide 85: Conclusion and Future Work

## Slide 86: System Overview and Recap
Transmitter

## Slide 87: Extrapolation to Underwater Regime
Transmitter

## Slide 88: Recommendations for Future Work
Transmitter

## Slide 89: Accomplishments
Transmitter

## Slide 90: Questions